| MOD STD |  | DWG.NO. | P-P-026-02-01-0 |  |
| --- | --- | --- | --- | --- |

BY153-122

# SPECIFICATIONS

| MODEL ITEMS | BY153-122 |
| --- | --- |
|  | ADC85~264 V |
| 1 | NOMINAL OUTPUT VOLTAGE | V | V1 | V2 | V3 |
|  |  |  | 5.0 | 12 | -12 |
| 2 | MAXIMUM OUTPUT CURRENT(CONVECTION) | A | 2 | 0.2 | 0.2 |
| 3 | MAXIMUM OUTPUT POWER (CONVECTION) | W | 14.8 |
| 4 | EFFICIENCY(TYP)(*1) | - | 70% |
| 5 | INPUT VOLTAGE RANGE | - | ADC85~264 V AC（47~63）HZ |
| 6 | INRUSH CURRENT(TYP) | A | 15A at 100VAC,30A at 200VAC,Ta=25℃,Cold Start. |
| 7 | DC OUTPUT VOLTAGE SETTING | V |  |  |  |
| 8 | OUTPUT VOLTAGE PRECISION (*2) | - | 4.95-5.10 | 11～13 | 11～13 |
| 9 | MAXIMUM LOAD REGULATION(*2) | - | 4.95-5.10 | 11～13 | 11～13 |
| 10 | MAXIMUM LINE REGULATION(*2) | - | 4.95-5.10 | 11～13 | 11～13 |
| 11 | MAXIMUM RIPPLE NOISE | - | 1% OR ≤100 mV |
| 12 | POLARITY |  | V1 substantive;V2,V3 together |
| 13 | OVER SHOOT | V | 10% |
| 14 | OVER POWER PROTECTION | - | >120% |
| 15 | OVER VOLTAGE PROTECTION(TPY) | V | TVS clamping at 6.8V |  |  |
| 16 | HOLD-UP TIME(TYP)(*3) | mS | 10(60% LOAD AT DC220V) |
| 17 | LEAKAGE CURRENT | mA | 0.75Ma MAX,0.2mA(Typ) at100VAC/0.44mA at230VAC |
| 18 | OPERATING TEMPERATURE | - | -10℃~＋70℃(-10~+50℃:100%,+60℃:60%,+70℃:50%) |
| 19 | STORAGE TEMPERATURE | - | -25~+75℃ |
| 20 | WITHSTAND VOLTAGE (*4) | - | INPUT-PE;INPUT-OUTPUT: 2.5KVAC 1min. OUTPUT-PE: 0.5KVAC 1min . |
| 21 | SAFETY | - | REFER TO GB4943,UL1950,IEC380 |
| 22 | CONDUCTED EMISSION |  | REFER TO IEC60255-22-6:2000 |
| 23 | ISOLATION RESISTANCE | - | MORE THAN 100MΩAT 25℃ |
| 24 | WEIGHT(TYP) | Kg | 0.5 |
| 25 | SIZE(W*H*D) | mm | REFER TO OUTLINE DRAWING(62*45*22mm) |
| NOTES: *1.BEFORE ADC INPUT ,TURN VR FULLY CLOCKWISE *2. V1,V2,V3 AT 0%,50%,100%LOAD. *3. AT 60% LOAD TO TEST. *4. LEAKAGE CURRENT 10mA |
| DWG | GYB | CHK |  | APPD |  |

# Comments

标准输出电压

过压保护

安全

传导

额定电压25℃，最大输出功率

其余回路等电位互相连接并接地（外壳）