产品特点Product features:

· 输入与输出不隔离设计

Input and output not insulation

· 输出恒流设计

Output constant current design

· 高恒流精度

Constant current high precision，

· 高功率因数

High PFC

· 高效率,高可靠性High efficiency, High Reliability

· 温度适用范围Temperature scope (-20-+70℃)

· 自然对流冷却Free Cooling,Without Extra Radiator

· 适用于LED照明及需要恒流供电的设备

Applicable to the LED illumination and need constant-current power equipment

技术规格 Specifications:

| 型号MODLE 项目Professional | HLPN10 |
| --- | --- |
| 输出Output | 恒流额定电压 Constant-current Nominal voltage | 66V |
|  | 恒流电压范围 Constant-current voltage range | 19-80V |
|  | 恒电流设定 Constant current setting | 150mA |
|  | 电流调节范围 Current adjustable range | 145-160mA |
|  | 纹波与噪音 Ripple & noise p-p | 3% |
|  | 空载输出电压 no-load voltage accuracy | 允许空载 |
|  | 线性调整率 Line regulation | ±5% |
|  | 输出过流保护 Output over current protection | 恒流限制The constant current limiting |
|  | 输出短路保护 Output short-circuit protection | 不能短路 |
| 输入 Input | 输入电压范围 Input voltage range | AC176——264V |
|  | 输入频率范围 Input Frequency range | 47——63Hz |
|  | 输入电流Input AC current | 根据输出电压变化而变化 |
|  | 输入功率Input power | 3.5-13W |
|  | 功率因数Power Factor | PF >0.75（Vo>50V,Vin=220VAC） |
|  | 效率Efficiency | >90%（Po=10W，Vin=220VAC） |
|  | 浪涌电流 Inrush Current | ＜10A/230VAC |
| 环境Environ- ment | 温度系数Temperature coefficien | <0.03%/℃ |
|  | 工作温度 Working temperature | -20-+70℃（参见图1See Figure 1） |
|  | 工作湿度Working humidity | 20-90%RH |
|  | 储存温度 Storage temperature | -40-+85℃ |
|  | 储存湿度Storage humidity | 20-90%RH |
|  | 冷却方式Cooling | 自然对流Nature cooling |
|  | 振动Vibration | 10-55Hz,19.6 m/s2,3分钟周期,沿X、Y、Z轴各60分钟 10-55Hz,19.6 m/s2,3minutes period,,60minutes each along X、Y and Z axis |
|  | 冲击Impact | 196.1m/s2 |
| 电磁兼容 与安规 Safety Standards and others | 耐压Hi-pot | 输入与输出不隔离 |
|  | 绝缘电阻 Insulation resistance | 输入与输出不隔离 |
|  | 安规Safety regulation | 输入与输出不隔离 |
|  | 电磁干扰Emission | According to EN 55015 |
|  | 电磁耐受 Immunity requirements | According to EN 61547 |
|  | 谐波电流Harmonic current | According to EN6100-3-2 |
| 结构Structure | 重量Weight | 50g |
|  | 尺寸Dimensions | 参见图2 See Figure 2 |
|  | 端子定义 Terminal Description | 参见图3 See Figure 3 |

附图Figure

附图1 ：输出功率与环境温度的降额曲线

Figure1：Output Power and Environmental temperature Derating curve.

- 附图2：结构尺寸

Figure2:Dimensions

`

- 附图3：端子定义

Figure 3:Terminal Description

| L | N | VO+ | VO- |
| --- | --- | --- | --- |
| 交流输入AC Input | 直流输出DC Output |

备注1：适用于LED照明及需要恒流供电的设备，需专业人员断电安装. 适合安装的设备必须是固定式，电源必须是安装在设备的内部.

Note1: Applicable to the LED illumination and need constant-current power equipment, need professional without electricity installation. Suitable to install the equipment must be fixed, Power supply must be installed on the inside of the equipment.